## Slide 1: LEAP Tutorial: FPGA Memory Abstractions
Michael Adler†, Kermin E. Fleming†,
Hsin-Jung Yang‡, and Felix Winterstein§
† Intel Corporation
‡ Massachusetts Institute of Technology
§ European Space Agency
September 1st, FPL 2015

## Slide 2: Memory Abstraction
#define U(t, x, y) array[2*(M*(y)+(x)) + (t)&1]
// memory allocation
int * array = (int*)malloc(M*N*2*sizeof(int));
// computation
for(int t = 0; t < T; t++)
for (int y = 0; y < N; y++)
for (int x = 0; x < M; x++)
U(t+1,x,y) = C0*U(t,x,y)
+ Cx*(U(t,x-1,y)+U(t,x+1,y))
+ Cy*(U(t,x,y-1)+U(t,x,y+1));
N
M
Memory allocation, read/write operations are easy
Complicated memory management is hidden behind the memory abstraction
General Purpose Processors
2D Heat Transfer

## Slide 3: Memory Abstraction
General Purpose Processors
int * array = (int*)malloc(M*N*2*sizeof(int));
d1 = array[a1];
array[a2] = d2;
Simple Program
Complex Memory Management
Ex: cache hierarchy, address translation,
page swapping….
How about FPGAs?

## Slide 4: FPGA Memory: Block RAMs
Block RAM
Engine
Interface
N
M
2D Heat Transfer
addr
din
wen
dout
for(int t = 0; t < T; t++)
for (int y = 0; y < N; y++)
for (int x = 0; x < M; x++)
U(t+1,x,y) = C0*U(t,x,y)
+ Cx*(U(t,x-1,y)+U(t,x+1,y))
+ Cy*(U(t,x,y-1)+U(t,x,y+1));
Difficulty:
Problem size cannot fit in block RAMs

## Slide 5: FPGA Memory Abstraction
N
M
2D Heat Transfer
addr
din
wen
dout
valid
Become Latency Insensitive
Difficulty:
Problem size cannot fit in block RAMs
Block RAM
Engine
Interface

## Slide 6: FPGA Memory Abstraction: LEAP Scratchpad
N
M
2D Heat Transfer
interface MEM_IFC#(type t_ADDR, type t_DATA)
method void readReq(t_ADDR addr);
method void write(t_ADDR addr, t_DATA din);
method t_DATA readResp();
endinterface
LEAP
Scratchpad
Engine
Interface
LEAP Scratchpad
Same memory interface
Arbitrary data size
Private address space
“Unlimited” storage
Automatic caching
M. Adler et al., “LEAP Scratchpads,” in FPGA, 2011.

## Slide 7: LEAP Scratchpad Hierarchy
Client
Client
Client
Interface
Processor
Application
L1 Cache
L2 Cache
Memory
Scratchpads
on-chip SRAM
on-board DRAM

## Slide 8: LEAP Scratchpad Usage
In C program:
int * array;
array = (int*)malloc((1<<28)*sizeof(int));
….
d1 = array[a1];
array[a2] = d2;
…
In LEAP program:
MEMORY_IFC(Bit#(28), Bit#(32)) memory <- mkScratchpad(scratchpadID, config);
….
memory.readReq(a1);
Bit#(32) d1 <- memory.readResp();
memory.write(a2, d2);
….
address space
data size
address space
data size

## Slide 9: LEAP Scratchpad Performance
Local Cache
Central Cache
Host Memory

## Slide 10: Scratchpad Optimization
Abstraction Enables Optimization
Reduce scratchpad latency
-> Automatic speed up memory-using programs
Leverage unused resources
Learn from optimization techniques in processors
  Larger caches, greater associativity
  Better cache policies
  Cache prefetching

## Slide 11: Optimization: Scratchpad Prefetcher
H. Yang et al., “Optimizing under Abstraction: Using Prefetching to Improve FPGA Performance,” in FPL, 2013

## Slide 12: Prefetching on FPGAs
Easier:
  Cleaner streaming memory accesses
  No need for PC as a filter to separate streams
  Fixed (usually plenty of) resources
Harder:
  Back-to-back memory accesses
  Inefficient to implement CAM
Scratchpad prefetcher uses address-based stride prefetching with a larger set of direct-mapped learners

## Slide 13: Prefetch Performance
K. Fleming et al., “H.264 Decoder: A Case Study in Multiple Design Points,” in MEMOCODE, 2008
Area requirements of FPGA prefetching are small.
  less than 0.5% of total chip area on the ML605 board
automatic speedup!

## Slide 14: Scratchpad Configurability
Client
Interface
Whether to instantiate a prefetcher
Private cache size
Whether to have a private cache
Whether to have the whole cache hierarchy

## Slide 15: LEAP Shared Memories

## Slide 16: Parallel Programming on FPGA
Goal: simplifying parallel programming on FPGAs
2D Heat Transfer Equation
N
M
for(int t = 0; t < T; t++){
#pragma omp parallel num_threads(4){
int thread_id = omp_get_thread_num();
int bid_x = thread_id%2;
int bid_y = thread_id/2;
for (int y = bid_y*(N/2); y < (1+bid_y)*(N/2); y++)
for (int x = bid_x*(M/2); x < (1+bid_x)*(M/2); x++)
U[t+1,x,y] = C0*U[t,x,y]
+ Cx*(U[t,x-1,y]+U[t,x+1,y])
+ Cy*(U[t,x,y-1]+U[t,x,y+1]);
}
}
operation on the shared array
implicit barrier synchronization

## Slide 17: Parallel Programming on FPGA
Goal: simplifying parallel programming on FPGAs
2D Heat Transfer Equation
How to implement on FPGAs?
N
M

## Slide 18: Parallel Programming on FPGA
2D Heat Transfer Equation
Engine1
Shared Memory
Engine2
Shared Memory
Engine3
Shared Memory
Engine4
Shared Memory
Interface
Coherence, Consistency, Synchronization
unlimited address space
Engine
arbitrary data size

## Slide 19: Parallel Programming on FPGA
2D Heat Transfer Equation
N
M
Engine 1
Engine 2
Engine 3
Engine 4
Interface
Difficulty: Performance is limited
Serialized requests
Long latency if across FPGAs
Remote Access

## Slide 20: Parallel Programming on FPGA
2D Heat Transfer Equation
N
M
Engine 1
Engine 2
Engine 3
Engine 4
Interface
Cache
Cache
Cache
Cache
Need cache coherence!

## Slide 21: LEAP Shared Memory Services: Coherent Scratchpad (CS)
Shared data ca
Store owner-bit information for every address
Store data
Ordering point
Ring-based snoopy protocol
Modified MOSI protocol
Engine
Interface
Engine
Engine
Engine
Shared Cache
pre-order request
ordered request
response
Coherent Scratchpad Controller
Ordering point
Store data
Store owner-bit information
data
owner bit
H. Yang, “LEAP Shared Memories: Automating the Construction of FPGA Coherent Memories,” in FCCM, 2014.

## Slide 22: LEAP Shared Memory Services: Coherent Scratchpad

## Slide 23: Parallel Programming on FPGA
2D Heat Transfer Equation
N
M
for(int t = 0; t < T; t++){
#pragma omp parallel num_threads(4){
int thread_id = omp_get_thread_num();
int bid_x = thread_id%2;
int bid_y = thread_id/2;
for (int y = bid_y*(N/2); y < (1+bid_y)*(N/2); y++)
for (int x = bid_x*(M/2); x < (1+bid_x)*(M/2); x++)
U[t+1,x,y] = C0*U[t,x,y]
+ Cx*(U[t,x-1,y]+U[t,x+1,y])
+ Cy*(U[t,x,y-1]+U[t,x,y+1]);
}
}
operation on the shared array
implicit barrier synchronization
Finish the inner loop operations
  Computations complete
  Memory operations complete
Wait until all threads are finished

## Slide 24: LEAP Shared Memory Services: Memory Consistency
Block RAM/Private Scratchpad Interface
Coherent Scratchpad Interface
interface MEM_IFC#(type t_ADDR, type t_DATA);
method void readReq (t_ADDR addr);
method void write(t_ADDR addr, t_DATA data);
method t_DATA readResp();
// t_REQ r := {READ, WRITE, FULL}
method Bool requestPending(t_REQ r);
endinterface
Fence support (memory consistency)
interface MEM_IFC#(type t_ADDR, type t_DATA);
method void readReq (t_ADDR addr);
method void write(t_ADDR addr, t_DATA data);
method t_DATA readResp();
endinterface

## Slide 25: Coherent Scratchpad Usage
Coherence Controller

## Slide 26: Parallel Programming on FPGA
2D Heat Transfer Equation
N
M
for(int t = 0; t < T; t++){
#pragma omp parallel num_threads(4){
int thread_id = omp_get_thread_num();
int bid_x = thread_id%2;
int bid_y = thread_id/2;
for (int y = bid_y*(N/2); y < (1+bid_y)*(N/2); y++)
for (int x = bid_x*(M/2); x < (1+bid_x)*(M/2); x++)
U[t+1,x,y] = C0*U[t,x,y]
+ Cx*(U[t,x-1,y]+U[t,x+1,y])
+ Cy*(U[t,x,y-1]+U[t,x,y+1]);
}
}
operation on the shared array
implicit barrier synchronization
Finish the inner loop operations
  Computations complete
  Memory operations complete
Wait until all threads are finished

## Slide 27: Synchronization Services: Memory Barrier
In Processor: software through-memory barriers
  via shared memory & locks
void barrier(num_threads_const, lock_addr, eflag_addr,
lflag_addr, ecounter_addr, lcounter_addr)
{
while (*eflag_addr);
lock(lock_addr);
(*ecounter_addr)++;
if ((*ecounter_addr) == num_thread_const){
(*eflag_addr) = 0;
(*lflag_addr) = 1;
}
unlock(lock_addr);
while (*lflag_addr);
lock(lock_addr);
(*lcounter_addr)++;
if ((*lcounter_addr) == num_thread_const){
(*lcounter_addr) = 0;
(*ecounter_addr) = 0;
(*eflag_addr) = 1;
(*lflag_addr) = 0;
}
unlock(lock_addr);
}

## Slide 28: Synchronization Services: Memory Barrier
Mask
Client A
Client B
Client C
Synchronization Client
Synchronization Client
Synchronization Client
Synchronization Controller
A
isDone
In Processor: software through-memory barriers
  via shared memory & locks
In FPGA:
barrierInit
Suppose clients A & B need to synchronize
B
isDone
allDone
barrierInit
void barrier()
{
send(isDone);
while (receive(allDone));
}
A
B
C

## Slide 29: Synchronization Services: Memory Barrier
In Processor: software through-memory barriers
  via shared memory & locks
In FPGA:
  outside of shared memory
Performance Comparison:
System | Barriers per Second | Normalized Throughput
LEAP Barrier Service | 7352076 | 342
Hardware Lock Barrier via Coherent Scratchpad | 85088 | 4
Spin-Lock Mutex-Enabled Cache* | 21510 | 1
* V. Mirian and P. Chow, “Managing mutex variables in a cache-coherent shared-memory system for FPGAs,” in FPT, 2012.

## Slide 30: LEAP Barrier Usage
interface BARRIER_IFC;
method Bool initialized();
method void setBarrier(t_BARRIER barrier);
method void barrierReached();
method void waitForSync() if (all nodes have reached the barrier);
endinterface

## Slide 31: Synchronization Services: Lock
Processor:
  through-memory locks
Performance Comparison (Shared Queue Test) :
LEAP lock primitive:
  hardware locks
Primitive | Normalized Performance
Global Arbiter | 2.19
LEAP Hardware Lock | 1.82
Through-Memory Software Lock | 1

## Slide 32: LEAP Lock Usage
interface LOCK_IFC#(type t_LOCK_ID);
method void acquireLockReq(t_LOCK_ID id);
method t_LOCK_ID lockResp() if (it receives lock); method void releaseLock(t_LOCK_ID id);
endinterface
Client A
LOCK_IFC#(Bit#(1)) lock <-
mkLockNode(groupID, MASTER);
lock.acquireLockReq(0);
if (lock.lockResp() == 0) // wait
begin
…….
// perform task
…….
end
lock.releaseLock();
Client B
LOCK_IFC#(Bit#(1)) lock <-
mkLockNode(groupID, SLAVE);
lock.acquireLockReq(0);
if (lock.lockResp() == 0) // wait
begin
…….
// perform task
…….
end
lock.releaseLock();
Client C
LOCK_IFC#(Bit#(1)) lock <-
mkLockNode(groupID, SLAVE);
lock.acquireLockReq(0);
if (lock.lockResp() == 0) // wait
begin
…….
// perform task
…….
end
lock.releaseLock();

## Slide 33: Performance on 2D Heat Transfer
FPGA: Xilinx VC707 Frame Size: 512x512
Coherent Cache Size: 8KB
Pixel Size: 8bit
N
M
Centralized Scratchpad
Coherent Scratchpad