## Slide 1: Bluespec Bare Minimum
Michael Adler

## Slide 2: Bluespec Philosophy
Programs are:
  State elements
    Registers
    Memories
    Clocks
    Wires (wrapped Verilog)
  Operations on those elements
Counter
Incr
Decr
Value
Bluespec must:
  Provide a way to declare state
  Define operations on state
  Wrap the state/operations in modular and composable units
  Define operations on modules
Notes: Counter is a register (the state)
Incr/Decr are operations on the register
Value is a method for reading the state

## Slide 3: Execution Model
General Purpose Computer
  Turing machine: Instruction pointer defines control flow
  Operates on global state
  Simple spatial parallelism: Multi-core or socket system adds parallel instruction pointers
Bluespec
  Spatially parallel: Sea of independent computation islands (rules)
  Rules operate on relatively local state
  Arbitration (scheduling) for rules that operate on shared state
Notes: A correct Bluespec program could, in theory, have all rules operating on global state. This would, however, generate very inefficient hardware since only one rule could fire at a time. A general purpose machine, running at higher frequency, would probably be faster.

## Slide 4: Bluespec Programs: Rules and Methods
  Rules (GAA)
    Guarded: May fire when predicate is true
    Atomic: Entire rule executes in one cycle and side effects visible at the start of the next cycle
    Rule scheduler built automatically by Bluespec
      Honors predicates
      Honors inter-rule conflicts
    Internal to modules
  Methods
    A module’s public functions
    Invoked by parent module’s rules or methods
Counter Module
Rule: Update Counter new_val = ctr; if (incr) new_val += 1; if (decr) new_val -= 1; ctr <= new_val;
Method: INCR
Method: DECR

## Slide 5: Random Syntactic Details
  Hash (#) disambiguates sets of parenthesized lists, e.g.: module mkFoo#(String fileName) (FOO_INTERFACE#(t))
  Arrows indicate side effects on the right-hand side: Reg#(Bit#(5)) r <- mkReg(0);
  Arrow assignment indicates a change to persistent state: r <= 3;
  Bare equal sign indicates no persistent side effects (can be evaluated at compile time – static elaboration): Bit#(5) r = 3;

## Slide 6: Data: Tagged Union
  Very common in Bluespec
  State is union of values + tag
typedef union tagged { void Invalid; t_DATA Valid; } Maybe#(type t_DATA) deriving (Bits);
Maybe#(Bit#(5)) x = tagged Valid 3; Maybe#(Bit#(5)) x = tagged Invalid;
if (m_v matches tagged Valid .v) begin f(v); end function isValid(Maybe#(t) m) if (m matches tagged Valid .dummy) return True; else return False; endfunction
Notes: Bluespec has the derived types you would expect, like struct.
Tagged union is a struct with names for each element and a tag that is an enumeration of all the tags
Note some features of function isValid:
  No return type is specified. The compiler figures out that it must be Bool.
  The type of argument “m” is polymorphic. Any type wrapped in a Maybe#() is acceptable.

## Slide 7: Interfaces
  Analogue of public C++ class interface
  May be polymorphic (type t in this case). Specific instances:
    FIFO#(Bit#(5))
    FIFO#(Maybe#(Bit#(2))
interface FIFO#(type t); method Action enq(t val); method Action deq(); method t first(); endinterface
Polymorphic type

## Slide 8: Modules
  Analogue of class implementations
  Methods correspond exactly to interface
  Modules may have internal state and rules
module mkFIFO (FIFO#(t)) provisos (Bits#(t, t_SZ)); method Action enq(t val); … endmethod method Action deq(); … endmethod method t first(); … endmethod endmodule
Module’s name
Module’s interface
Constraints on t
Notes: Note the lack of # after mkFIFO. The interface is separate from the module name. If the module has arguments (e.g. passing a string to name the FIFO for debugging) it would appear as:
module mkFIFO#(String name) (FIFO#(t)).
For clarity, we usually write modules:
module mkFIFO // Interface: (FIFO#(t));
…
endmodule

## Slide 9: State
  Instantiated inside modules
  State is wrapped by module interfaces. Bluespec provides primitives:
    mkReg() Interface: Reg#(t)
    mkBRAM() Interface: BRAM#(a, t)
  User code can declare more primitives, ultimately implemented in Verilog
module mkFIFO (FIFO#(t)) provisos (Bits#(t, t_SZ)); Reg#(Vector#(2, t)) data <- mkReg(?); Reg#(Bit#(2)) nActive <- mkReg(0); … endmodule

## Slide 10: FIFO Implementation
module mkFIFO (FIFO#(t)) provisos (Bits#(t, t_SZ)); Reg#(Vector#(2, t)) data <- mkReg(?); Reg#(Bit#(2)) nActive <- mkReg(0); Reg#(Bit#(1)) enqNext <- mkReg(0); Reg#(Bit#(1)) deqNext <- mkReg(0); method Action enq(t val) if (nActive < 2); data[enqNext] <= val; enqNext <= enqNext + 1; nActive <= nActive + 1; endmethod method Action deq() if (nActive != 0); deqNext <= deqNext + 1; nActive <= nActive - 1; endmethod method t first() if (nActive != 0); return data[deqNext]; endmethod endmodule
  This is not optimal, just example
    enq/deq are mutually exclusive
    nActive could be replaced by notEmpty

## Slide 11: FIFO Implementation with LUTRAM Storage
module mkFIFO (FIFO#(t)) provisos (Bits#(t, t_SZ)); LUTRAM#(Bit#(1), t) data <- mkLUTRAMU(); Reg#(Bit#(2)) nActive <- mkReg(0); Reg#(Bit#(1)) enqNext <- mkReg(0); Reg#(Bit#(1)) deqNext <- mkReg(0); method Action enq(t val) if (nActive < 2); data.upd(enqNext, val); enqNext <= enqNext + 1; nActive <= nActive + 1; endmethod method Action deq() if (nActive != 0); deqNext <= deqNext + 1; nActive <= nActive - 1; endmethod method t first() if (nActive != 0); return data.sub(deqNext); endmethod endmodule
  Basically the same code
  Data storage module and interface changed

## Slide 12: Rules and Functions
module mkCounter#(Bit#(nBits) initialValue) // Interface: (COUNTER#(nBits)); // Counter value Reg#(Bit#(nBits)) ctr <- mkReg(initialValue); PulseWire upW <- mkPulseWire(); PulseWire downW <- mkPulseWire(); function newValue(); let new_val = ctr; if (upW) new_val = new_val + 1; if (downW) new_val = new_val - 1; return new_val; endfunction rule updateCounter; ctr <= newValue(); endrule
method Bit#(nBits) value(); return ctr; endmethod method Action up(); upW.send(); endmethod method Action down(); downW.send(); endmethod endmodule
  Rules operate inside modules on internal state
  Triggered by Bluespec-generated scheduler (computes canFire and willFire)
  Rules are atomic (GAA – guarded atomic actions)

## Slide 13: Rule Scheduling
module … Reg#(Bit#(5)) ctr <- mkReg(0); PulseWire resetW <- mkPulseWire(); rule incr (if !resetW); ctr <= ctr + 1; endrule rule rst (if resetW); ctr <= 0; endrule … endmodule
  Rules incr and rst are mutually exclusive because of ctr write.
  Here the scheduling predicate is explicit. Bluespec computes more complicated predicates implicitly. E.g.:
    Can’t deq() a FIFO that is empty.
    Two rules can’t enq() to a FIFO in the same cycle. Bluespec picks a static priority if necessary.
    A rule’s predicate includes the conjunction of the predicates of all methods it invokes.

## Slide 14: Side Effects at END of Cycle
  The order of statements in a rule doesn’t matter
  All updates are visible only at the end of a cycle
  These are equivalent:
rule swapA; rule swapB; x <= y; y <= x; y <= x; x <= y; endrule endrule
  These are equivalent:
fifo.deq(); let x = fifo.first(); let x = fifo.first(); fifo.deq();

## Slide 15: Static Elaboration
  Loops will be unrolled statically at compile time
  Hard at first – you will get used to it
Vector#(16, Reg#(4)) v <- replicateM(mkReg(0)); rule shiftIn (m_nv matches tagged Valid .nv); for (Integer i = 0; i < 15; i = i + 1) begin v[i] <= v[i + 1]; end v[15] <= nv; endrule

## Slide 16: Beware of Simple Syntax with Big Consequences
  Most important difference from C programming is you must learn to imagine the generated hardware
Reg#(Vector#(2048, Bit#(8))) r <- mkReg(?); r[x] <= r[y] + 1; Vector#(2048, Reg#(Bit#(8))) v <- replicateM(mkReg(?)); v[x] <= v[y] + 1; LUTRAM#(Bit#(11), Bit#(8)) lr <- mkLUTRAMU(); lr.upd(x, lr.sub(y) + 1);
Read 8*2048 bits, two MUXes, write 8*2048 bits
Probably uses a RAM
Definitely uses a RAM