## Slide 1: The LEAP FPGA Operating System
Kermin Fleming
Michael Adler

## Slide 2: A Bit of History
  LEAP: Latency-insensitive Environment for Application Programming
  Development of LEAP began ~7 years ago
    Intel: FPGA-based performance models (HAsim)
      Michael Adler, Joel Emer, Angshuman Parashar, Michael Pellauer
    MIT: Wireless transceivers and other IP blocks
  Open source (BSD License)
  Growing community:

## Slide 3: What is General Purpose Computing?
  Not the ISA (x86, ARM, Power…)
  Not the operating system (Unix, Windows, CP/M)
  General purpose computing is programmability
    Enables even novice programmers to build powerful programs

## Slide 4: Where Does Programmability Come From?
User Program
  Programming languages
    Both high- and low-level
  Services with consistent interfaces (e.g. POSIX)
    Memory management (malloc, mmap)
    Message formatting and printing (stdio)
    Communication channels (pipes, TCP/IP)
  Kernel abstraction
    Consistent driver interfaces hide device hardware variations
    Virtual memory eliminates machine-specific memory management
libc libraries
Kernel
Devices
printf(“hello world”);

## Slide 5
  Imagine I give you a CPU with a new ISA and I/O devices.
  Do you:
    Write your application and drivers in assembly language?
    Write an LLVM backend and port Linux?

## Slide 6: FPGAs aren’t general purpose!
  Why? We usually pick option A!
    Driver interfaces are platform-specific (wires).
    Building blocks are low level:
      Memories provided only as drivers
      I/O provided as raw channels
    Driver interface and timing details leak into user code.
    Standard programming languages are very low level
Achieving option B requires an operating environment.

## Slide 7: Hello World on Processor
        main() { printf(“Hello world!\n”);
        }
Notes: User expects:
* Universal: works on any OS because LIBC provides a common API independent of the kernel interface
- User space buffering and memory management
- User program shares address space with I/O library
* Trap to kernel when needed with automatic memory management
* Automatic binding of file handle to some device
- Disk file system
- Network socket

## Slide 8: Hello World on FPGA?
        $write(“Hello world!\n”);
Notes: User expects:
  Same as C (inside software simulators)
Nothing on hardware!

## Slide 9: Hello World on FPGA
(Excerpt from 300 page Xilinx 7 Series PCIe Manual)
  AAAAAAAAAAAAAAAAAH!
  All the software programmers resigned in protest

## Slide 10: Hello World in LEAP
        module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
        endmodule
Notes: An entire LEAP application.
What is not pictured is the virtual platform that sends the start message, receives the finish signal and provides the STDIO library. This is just like standard programming, which wraps main() in crt0 and provides libc.

## Slide 11: What do we get from operating environments?
  Programmers no longer need to focus on infrastructure
    Greatly reduced design time, simplified designs
  Advances are shared by all programs
    New memory systems, scheduling policies, etc.
  Wide portability
    Enabled by common interfaces
  What about HLS, OpenCL, etc.?
    Promising languages, lots of productivity, etc.
    Java and C++ don’t implement OS kernels
    All programming environments benefit from a shared OS

## Slide 12: Requirements of any operating environment
  Allow application to expose high-level needs
    Memory, communication, devices
    Operating system responsible for satisfying these needs
  Maintain the expressivity of programs
    Programmers should decide how to express programs, not OS
  Satisfy these requirements with light-weight, user-friendly interfaces
Notes: Consequences of providing these functinoalities

## Slide 13: Latency-insensitive Channels: The core LEAP Abstraction

## Slide 14: How do user programs and OS interface in software?
User Program
  User-OS interaction usually involves manipulations through
    Function calls
    Memory and register!
    Very natural for von Neumann machines
  Details of machine are hidden through abstraction layers
    User: function call
    OS: hardware abstraction layer
libc libraries
Kernel
Devices
printf(“hello world”);
How can we achieve a similar layering in FPGAs?
Notes: This is a natural mechanism for von Neumann machines

## Slide 15: Memory is Not a Good Base Abstraction for FPGAs
  Spatial, distributed architecture
    Computational structures are small, dedicated
    Most algorithms follow pipelines
  Memory sharing is possible, but expensive
    Costs time, area, or both

## Slide 16: Communication: A Natural Abstraction for FPGAs
Inter-module communication by defined protocol
    Usually FIFO-like
    Nearly all HW designs use this methodology
  What if we abstract this communication?
mkB
FPGA
mkC
mkA
Notes: Look at 8/9 transition
Recently, latency-insensitive design has become popular as a way to implement hardware. In LI design, programs are separated into modules which communicate solely by way of latency insensitive channels. These channels are implemented as simple hardware FIFOs. Designs are written so that computation only occurs when data is available in ingress FIFOS or when there is space for output in egress FIFOs. LI designs enjoy many benefits including improved modular composition and simplified design space exploration.

## Slide 17: Abstracting Communication: From Register to FIFO
Not Full
  Communications have two components:
    Payload (message contents)
    Timing
      When wires have payloads
      When payload ownership is transferred
Data In
Data Out
Enq
Not Empty
Deq
Registers
Clock
Systolic Pipeline
Latency-Insensitive Pipeline
FIFO
Clock
Data In
Data Out
Not Empty
Enq
Deq
D0
D0

## Slide 18: But the FIFO isn’t quite enough
  FIFOs do a good job of decoupling FPGA programs
    But not sufficiently abstract
    Programmer may really require specific latency and buffering
  Need to add a little more abstraction
Not Full
Data
Data
Enq
Not Empty
Deq
Clock
Latency-Insensitive Pipeline
FIFO
Clock
Data In
Data Out
Not Empty
Enq
Deq
D0
D0

## Slide 19: Latency-Insensitive Channels: The Core LEAP Abstraction
Physical
Transport
  What if I abstract the notion of communication?
  Introduce new RTL primitive: Latency-insensitive Channel
    Channel has send/receive, flow controlled interface
    Guaranteed FIFO delivery
  But no explicit notion of implementation
    LEAP picks implementation to suit program needs
Not Full
Data
Data
Enq
Not Empty
Deq
Clock
Latency-Insensitive Pipeline
Recv
Send
Latency-Insensitive Channel
Clock
Data In
Data Out
Not Empty
Enq
Deq
Send
Recv
D0
D0
D0
D0

## Slide 20: Abstract Communications: What does it buy us?
  Programmers see a simple, consistent interface to the operating environment
    LI Channels strongly resemble existing hardware constructs
    User program decoupled from devices, ensuring portability

## Slide 21: Abstract communications: Heterogeneous platforms
  Software can be viewed as a very slow channel endpoint
FPGA
User
IP
User
Software
mkSend(“toFPGA”)
mkRecv(“toFPGA”)
mkRecv(“fromFPGA”)
mkSend(“fromFPGA”)
CPU

## Slide 22: Abstract Communication Abstracts Devices
  Developer/user program need not comprehend physical device
    Or implement a complex stack
    Devices managed by LEAP, ensuring portability
user code
CPU
mkSend(“toFPGA”)
Used Counts
Header
mkRecv(“toFPGA”)
Inter-Device
PHY
Soft Service Paring
Channel Marshalling
Driver Thread
Communication Thread
FPGA
FPGA
CPU

## Slide 23
FPGA
FPGA1
FPGA0
Exe
Decode
Fetch
mkC
Exe
Decode
Fetch
mkB
Control
mkA
Abstract communication permit LEAP to automatically partition any design.
Partitioning LI Channels Across FPGAs
Notes: From our perspective, the important property of LI designs is that they do not care long it takes for data to propagate through the FIFOs. This allows us to solve many of the problems of existing multifpga tools: we no longer need to maintain a global notion of clock; in some sense data communication naturally synchronizes the design. Leveraging this property, it is logically straightforward to partition LI designs among FPGAs: we simply implement FIFOs across the FIFO boundaries. So now we’re done, right?

## Slide 24: Abstract Communication Enables Automated Multi-FPGA Compilation
Used Counts
FIFO 0
FIFO 1
FIFO 2
FIFO 3
AM
Head Ptr
Tail Ptr
Free Counts
FIFO 0
FIFO 1
FIFO 2
FIFO 3
AM
FIFO 0
FIFO 1
FIFO 2
FIFO 3
AM
Used Counts
Head Ptr
Tail Ptr
Free Counts
Used Counts
Head Ptr
Tail Ptr
Free Counts
Channel VC Buffering
Lane Demerging
Lane Merging
Channel Arbitration
Recv A
Recv B
Recv C
Recv B
Recv A
Recv B
Recv C
Recv B
Recv A
Recv B
Recv C
Recv B
Channel Marshalling
Recv A
Recv B
Recv C
Recv B
Recv A
Recv B
Recv C
Recv B
Recv A
Recv B
Recv C
Recv B
Channel Demarshalling
Physical Interconnect
Deserialize/Reliability
CRC
Serialize/Reliability
FIFO 0
FIFO 1
FIFO 2
FIFO 3
AM
CRC
mkRecv(“toFPGA0”)
mkSend(“toFPGA0”)
FPGA0
FPGA1
  User programs need not comprehend execution on same device!

## Slide 25: Multiple Expectations
Chart: Modulation Scheme
| BPSK | QPSK | QAM-16 | QAM-64
Hardware Channel Model | 2.3 | 1.6 | 1.6 | 1.6
Multiple FPGAs Mean More Resources
Larger Designs – up to 10x!
Chart: Simulated Cores
| 8 | 16 | 25 | 36 | 49 | 64 | 81 | 100 | 121
Single FPGA | 6853253 | 6790058 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dual FPGA (Max. 16) | 3992817 | 5449854 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dual FPGA (Max. 64) | 3848363 | 5256324 | 6449001 | 6930303 | 6394061 | 5681841 | 0 | 0 | 0
Dual FPGA (Max. 128) | 3331840 | 4730960 | 5701291 | 6078976 | 5621253 | 4713853 | 4456793 | 3699577 | 3434375
Faster Implementation – even superlinear!
Notes: A single FPGA is sufficient for simulation. However, if the simulation is partitioned between FPGAs, it can be much faster, in part because improved access to FPGA resources permits much high clock frequencies. Here, improved clock frequency results in a super linear speed up, in some cases. Also, partitioned simulation has another advantage: fast compile times.

## Slide 26: Communications: A Fundamental Service
  Latency-insensitive channels enable any development environment
    No assumption about program source, so long as LI channels are used
    Operating systems still run assembly
  Potential for common interface among programming languages
    Verilog/VHDL, Bluespec
    HLS compilers
    Software: C, C++

## Slide 27: LEAP Service Libraries: Making the FPGA Programmable

## Slide 28: Service Libraries
  Communications is the fundamental kernel layer
    But programmers also benefit from services libraries
  Operating systems usually ship with many useful libraries

## Slide 29: What I really want is to write code
STDIO#(Bit#(64)) stdio <- mkStdIO();
let msgDone <- getGlobalStringUID("heat: done cycle: %016ld, test cycle count: %016ld\n");
rule sendDone (state == STATE_finished); stdio.printf(msgDone, list2(zeroExtend(cycleCnt), zeroExtend(cycleCnt-initCycleCnt))); state <= STATE_exit; endrule
Don’t want to understand how library works

## Slide 30: Services: Processor vs. FPGA
 | Processor | FPGA
Implementation | Instructions in library | Spatially distributed
Invocation | Call an address | Message over wires
Data Transfer | Global Memory | Message over wires
  LEAP services take a client-server architecture
    Conveniently layered on LI Channels
    Composition enables rapid development of sophisticated libraries

## Slide 31: STDIO: A Service Library in FPGA
FPGA
STDIO
Service
        User Program
Request 0
Response 0
Request n
Response n
…
CPU
  But what if application needs more than one client?
    Software can share a single library code
    Spatial nature of FPGAs requires services to be distributed
Software STDIO
        let msg <- getGlobalStringUID("Hello, World!\n");
        stdio.printf(msg, List::Nil);
LI Channels

## Slide 32: A Scalable Service Architecture: Multiple Clients
FPGA
Local STDIO
Client 0
Request 0
Response 0
Request n
Response n
…
Local STDIO
Client 1
Request 0
Response 0
Request n
Response n
…
Global STDIO
Software STDIO
CPU
Distributed services are transparent to user program
Notes: Unlike software where a single library can be shared, in spatial architecture we need to instantiate multiple clients

## Slide 33: A Scalable Service Architecture: Multiple FPGAs
FPGA1
Local STDIO
Client 0
Request 0
Response 0
Request n
Response n
…
Local STDIO
Client 1
Request 0
Response 0
Request n
Response n
…
Global STDIO
Software STDIO
CPU
FPGA0
Notes: Unlike software where a single library can be shared, in spatial architecture we need to instantiate multiple clients

## Slide 34: LEAP Services

## Slide 35: LEAP Services
  Scratchpads (second half of the tutorial)
    Memory
    Locks
    Semaphores
  Dynamic parameters
    “Named” variables initialized at startup
    Implemented as a scan chain
  Debugging
    Automatic monitoring of all soft connection full / empty states
    User-extensions for adding other variables to monitor
    Scan and emit formatted output

## Slide 36: Questions?