## Slide 1: Hello World: Running a LEAP Program
Michael Adler Elliott Fleming
Hsin-jung Yang Felix Winterstein

## Slide 2: Getting Started

## Slide 3: Getting Started
  Logging in:
    User: leap
    Password: leap
  Environment
Environment setup script
Tutorial AWB workspace
Bluespec installation

## Slide 4: Hello World in LEAP

## Slide 5: Hello World in C
int main (int argc, char* argv[]) { printf(“Hello, world!\n”); return 0; }
What actions are taken by the system when compiling/executing this code?

## Slide 6: Hello World in LEAP
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule
This code is a complete LEAP program
hello-world.bsv

## Slide 7: Running AWB
  LEAP uses AWB to construct build scripts
  Start by executing the commands:
    cd tutorial export EDITOR=emacs awb
  We’ll use AWB for the tutorial
    GUI-less build option leap-make is a new, class-friendly feature

## Slide 8: Hello World in LEAP: Accessing the Code
More AWB Examples: https://github.com/AWB-Tools/awb/wiki/AWB-example-build-GUI
  LEAP uses AWB as a code management-facility
    AWB is not essential to using LEAP’s core functionalities
  AWB ‘models’ are FPGA program/target pairings
  Use edit to see the code included in the FPGA program

## Slide 9: Hello World in LEAP: A view of the code
  Here, we see the complete nest of code needed to run a basic LEAP program
  Only the Hello World module is the user program, everything else is LEAP OS.
Notes: Operations – replace module in tree, edit module, open shell in module’s source directory.

## Slide 10: Hello World in LEAP: Opening the Code
  Right clicking Hello World gives the option to edit the source code
  For the next few slides we’ll consider hello.bsv
  Often, a README will be included along with the code
Notes: Operations – replace module in tree, edit module, open shell in module’s source directory.

## Slide 11: Hello World in LEAP: Expected Behavior
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule
Hello, World!
  What do we expect when running Hello World?
    A print to screen…
  Like software, this print should happen no matter what our execution target:
    Simulation
    Single FPGA
    Multiple FPGA
  LEAP’s operating system and compilation facilities enable this expected behavior

## Slide 12: Hello World in LEAP: Latency-insensitive Modules
  LEAP programs are composed of latency-insensitive modules
    These modules communicate externally using latency-insensitive channels
    mkConnectedApplication is a latency insensitive module, and is similar in function to C’s main
    Sub-modules like stdio can have arbitrary interfaces, including LI channels.
    Three kinds of modules:
      LI Modules (channel interface only)
      Non-LI Modules (non-channel only)
      Hybrid (Both channel and non-channel interfaces)
  LI modules can have non-latency-insensitive components like registers, wires, and arbitrary logic
Hidden LI
Interface
Arbitrary Wire Interface
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule

## Slide 13: Hello World in LEAP: Where are the Channels?
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule
  mkConnectedApplication is a latency-insensitive module
    But where are the interface latency-insensitive channels?
    The LEAP compiler uses SoftServices to manage special kinds of interfaces like memory and communication.
    Denoted with the [CONNECTED_MODULE] syntax
  mkConnectedApplication inherits the channels of STDIO
    The STDIO client uses a “chain”, the latency-insensitive broadcast primitive to talk to the STDIO server
module [CONNECTED_MODULE] mkSTDIO (); . . . Chain#(Bit#(64)) stdioNetwork <- mkChain(“STDIO”); . . . endmodule

## Slide 14: Hello World in LEAP: Handling Strings
  Hello World prints a string
  Strings are difficult to manage in hardware
    We borrow from software and use pointers
    SoftServices gives each string a unique ID at compile time
      Here, msg is a pointer to the string “Hello, World!”
      These string IDs are exported to software as a table, just like in C
      At run time, STDIO calls like printf pass the string pointer
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule

## Slide 15: Hello World in LEAP: The Anatomy of a Service
module [CONNECTED_MODULE] mkConnectedApplication ();
        STDIO#(Bit#(32)) stdio <- mkStdIO();
        let msg <- getGlobalStringUID("Hello, World!\n");
        Reg#(STATE) state <- mkReg(STATE_start);
        rule hello (state == STATE_start); stdio.printf(msg, List::nil);
        state <= STATE_finish; endrule
endmodule
  LEAP provides many useful services, which simplfy common programming tasks
    STDIO, locks, barriers, statistics, assertions, etc.
  Services take a client-server architecture
    Similar to SW operating system services
    User programs instantiate clients, like mkStdIO
    LEAP’s driver code instantiates a server which handles requests from clients
    Client are connected to the server by latency-insensitive channels
    Servers are often connected to SW by latency-insensitive channels.
STDIO Server (HW)
STDIO Server (SW)
Non-LI Ifc.
LI Ifc.
Hybrid Ifc.
FPGA
CPU

## Slide 16: Building on abstractions: STDIO Service
Virtual Channel Multiplexing
Kernel Driver
FPGA Physical Drivers
Virtual Channel Multiplexing
FPGA
CPU
Marshalling
Marshalling
STDIO Server
STDIO Server
STDIO
Client
User
Module
STDIO
Client
User
Module
STDIO
Client
User
Module
printf()
LI Network
stdio.printf(msg,List::nil);

## Slide 17: Service Portability: Abstraction Across Different Platforms
Virtual Channel Multplexing
ACP Physical Devices
Virtual Channel Multiplexing
FPGA
CPU
Marshaling
Marshaling
STDIO Service
STDIO Service
STDIO
Client
User
Module
STDIO
Client
User
Module
STDIO
Client
User
Module
printf()
stdio.printf(msg,List::nil);
Simulator
void channelToHost(long long data);
XUPV5 Physical Devices
Simulation Physical Devices
ACP Kernel Driver
XUPV5 Kernel Driver
Simulation Driver

## Slide 18: Building Hello World for Simulation (GUI)

## Slide 19: Hello World: Setting up the Build
The ‘configure’ button in the ‘Models’ tab sets up a series of SCons scripts which will be used to construct the application. hello_hybrid_exe targets simulation, hello_hybrid_vc707 targets the VC707, etc.

## Slide 20: Hello World: Setting Up the Build
Runlog shows the command line tool invoked. The leap-configure tool creates a build directory for the program.

## Slide 21: Hello World: Building the Code
The ‘build’ button in the build option tab invokes ‘scons’ in the build tree created by the configure script.

## Slide 22: Hello World: Setting Up a Run
The ‘setup’ button in the ‘benchmarks’ tab invokes the proper benchmark setup tool as determined by the model type. (See apm-edit for details)

## Slide 23: Hello World: Running Hello World
The ‘run’ button in the ‘Run Options’ tab invokes the ./run script in the benchmark directory created by the benchmark setup script. The run script manages loading the program targets (FPGAs, sw, etc)

## Slide 24: Hello World: Running Hello World
https://github.com/AWB-Tools/awb/wiki/AWB-example-build-GUI

## Slide 25: Building Hello World for Simulation (Command Line)

## Slide 26: Getting Started
  Sometimes it’s just nicer to build from the command line
  Start from tutorial home directory
Tutorial AWB workspace (start here)

## Slide 27: Finding the simulation build directory
  This directory is constructed when you ‘configure’ in AWB
  Each FPGA program will have its own directory
LEAP program build directories
Generated LEAP build script
AWB Workspace build configuration directory

## Slide 28: Building from Command Line
  AWB builds programs in the ‘pm’ directory
  LEAP uses scons as its build infrastructure

## Slide 29: Building from command line
  Typing scons builds the design
    Parameters can be set by typing them on the command line, as in “MODEL_CLOCK_FREQ=175”

## Slide 30: Simulating The Design
  AWB builds a simulation wrapper in the ‘bm’ directory
  Executing the ‘run’ command will invoke the hardware simulator and software side of the LEAP program.

## Slide 31: Setting Dynamic Parameters
  Hardware parameters can be set from the command line
  In this case, we force LEAP to dump debug information

## Slide 32: Questions?