## Slide 1: LEAP: Simplifying the construction of FPGA-based processor models
Michael Adler
Elliott Fleming
Michael Pellauer
Joel Emer

## Slide 2: FPGAs are hard to use
Slow tools with incomprehensible error messages
Complex, poorly documented physical interfaces
Lack of programming abstraction
Limited debugging interfaces
The goal of LEAP is to make FPGAs easier to use
+_+
-_-;;
;_;
T__T
o_O
:(
T_T
@_@
Notes: /needs a transition here
I believe in FPGAs as a driver of processing performance in the future. However, FPGAs are and remain difficult to use. Parallel programming itself is difficult, but even this is not the chief issue in using FPGAs. There are many aspects of design peculiar to FPGAs which are quite difficult. Among them, using device resources, debugging, dealing with discrepancies in the behavior of simulation and the FPGA. When I started working with FPGAs, this was the only I’ve been working lately with a few younger graduate students. Here are a few emoticons that they have used to describe their experiences in working with FPGAs in the last few days . Note that there’s a regional dialect. Korean and Chinese emoticons use different numbers of underscores. Clearly, they’re suffering. The goal of this thesis is to make FPGAs easier to use.

## Slide 3: What is LEAP?
Similar to an operating system, but with stronger compilation support
Useful for applications many applications, including processor modeling
User base in industry and academia

## Slide 4: Hello World in C
int main (int argc, char* argv[])
{
printf(“Hello, world!\n”);
return 0;
}
What actions are taken by the system when compiling/executing this code?

## Slide 5: Hello World in LEAP
module [CONNECTED_MODULE] mkConnectedApplication (); STDIO#(Bit#(32)) stdio <- mkStdIO(); Reg#(STATE) state <- mkReg(STATE_start); let msg <- getGlobalStringUID("Hello, world!\n”); rule hello (state == STATE_start); stdio.printf(msg, List::nil); state <= STATE_finish; endrule
endmodule
This code is a complete LEAP program

## Slide 6: What is LEAP?
LEAP = LINC-based Environment for Application Programming
  Flexible inter-module communication paradigm
  Connections that provide latency-insensitive communications
  A general memory paradigm
  Arbitrarily sized memory spaces (private or shared)
  System libraries, like STDIO, built on top of these abstractions

## Slide 7: Communications In LEAP
  Communications in FPGAs are a major headache
  Many interesting FPGA accelerators, including HAsim, require processor assistance
  FPGA-external communication is major headache
  FPGA users consistently reinvent drivers (PCIE, GigE, SERDES, …) and bake these drivers into their designs
  Painful debugging ensues
  LEAP decouple logical and physical communications using latency-insensitive channels
  Simple portable communication between FPGA and CPU or multiple FPGAs…
Notes: Flow is still not right here.

## Slide 8: What if a Model Doesn’t Fit on an FPGA?
FPGA
Optimize
Use bigger FPGA
Use multiple FPGAs
  Partition
  Map
  Network
FPGA
Fetch
I-Cache
Decode
Execute
Memory
D- Cache
Local
Commit
Communications module
Notes: Manual and automatic are not high level points
As we implement these algorithms for FPGA, it may be the case that an interesting design does not fit on the FPGA. For example, we may build a complex, next generation baseband or a large processor simulator. When this happens, we have a few choices. We can try to optimize the design or we can buy a bigger FPGA. However, for some designs we will ultimately have to use multiple FPGAs. Ultimately, this means solving three problems, which any multiple FPGA compiler must solve: partitioning the design somehow, mapping it to multiple FPGAs, and the synthesizing some communications network. In solving these problems, we have two choices. We can, of course, manually construct a multiple FPGA implementation. But just compounds the already painful FPGA design experience. Alternatively we can construct a tool that will solve the three problems for us.

## Slide 9: Latency-Insensitive Design: A Higher Semantic
Inter-module communication by latency insensitive channels
  Changing the timing behavior of a module does not affect functional correctness of the program
Many HW designs use this methodology
  Improved modularity
  Simplified design-space exploration
Implemented with guarded FIFOs in current RTLs
Control
Timing Partition
Exe
Decode
Fetch
FPGA
Functional Partition
Exe
Decode
Fetch
Control Partition
Notes: Look at 8/9 transition
Recently, latency-insensitive design has become popular as a way to implement hardware. In LI design, programs are separated into modules which communicate solely by way of latency insensitive channels. These channels are implemented as simple hardware FIFOs. Designs are written so that computation only occurs when data is available in ingress FIFOS or when there is space for output in egress FIFOs. LI designs enjoy many benefits including improved modular composition and simplified design space exploration.

## Slide 10
FPGA
FPGA1
FPGA0
Timing Partition
Exe
Decode
Fetch
Functional Partition
Exe
Decode
Fetch
Control
Control Partition
Because behavior of LI channels does not affect functional correctness, no inter-FPGA synchronization is required.
Latency-Insensitive Design: A Higher Semantic
Notes: From our perspective, the important property of LI designs is that they do not care long it takes for data to propagate through the FIFOs. This allows us to solve many of the problems of existing multifpga tools: we no longer need to maintain a global notion of clock; in some sense data communication naturally synchronizes the design. Leveraging this property, it is logically straightforward to partition LI designs among FPGAs: we simply implement FIFOs across the FIFO boundaries. So now we’re done, right?

## Slide 11
There are many FIFOs in the design
  It may not be safe to modify some of them
Compilers see only wires and registers
  Reasoning about cycle accuracy is difficult
Control
Timing Partition
Exe
Decode
Fetch
FPGA
Functional Partition
Exe
Decode
Fetch
Control Partition
But the programmer knows about the LI property…
Latency-Insensitive Design: A Higher Semantic
Notes: Well, not so fast. The difficulty in latency-insensitive design, from a compiler’s perspective, is that it is impossible to reason about. To the compiler, an LI FIFO is a bunch of registers and gates with fixed behavior, and there may be many FIFOs in the design. Even inserting one cycle into the design may break it. In general, proving that it is safe to modify the cycle-over-cycle behavior of a design is not possible.

## Slide 12: A Syntax for LI Design
Programmer needs to differentiate LI channels from normal FIFOs
Latency-Insensitive Send/Recv endpoints
  Implementation chosen by compiler
  FIFO order
  Guaranteed delivery
Explicit programmer contract
  Unspecified buffering & unspecified latency
  Programmer responsible for correct annotation
module mkTimeP;
Send#(Inst) send <- mkSend(“Decode”);
endmodule
module mkFuncP;
Recv#(Inst) recv <- mkRecv(“Decode”);
endmodule
mkFuncP
RTL
mkTimeP
RTL
Easy to use – often a textual substitution!
Notes: To solve this problem, we introduce a syntax for explicitly declaring latency-insensitive FIFOs. Here, programmers write down send and receive endpoints, which are matched by name. The compiler is free to choose whatever implementation that it would like between the endpoints. When instantiating the latency insensitive primitive, the programmer agrees to a specific contract: he will write his program in such a way that it can tolerate unspecified buffering and latency. The programmer is solely responsible for maintaining this guarantee.

## Slide 13: HAsim: Design Scaling
Good 
Chart: Simulated Cores
| 8 | 16 | 25 | 36 | 49 | 64 | 81 | 100 | 121
Single FPGA | 6.0195 | 6.1092 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dual FPGA (Max 16) | 3.726 | 5.1336 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Dual FPGA (Max 64) | 3.5969 | 4.9588 | 6.051 | 6.6477 | 6.3481 | 5.782 | 0 | 0 | 0
Dual FPGA (Max 128) | 3.1421 | 4.4571 | 5.3466 | 5.808 | 5.5904 | 4.9664 | 4.5913 | 4.023 | 3.7386
Notes: Let’s look at how HAsim performs when we scale to multiple FPGAs. The first thing to notice is that HAsim scales to 121 cores on two FPGAs. This superlinear scaling occurs because Hasim is time-multiplexed, and so only the state elements must be replicated. Here we measure performance in aggregate MIPS, the number of instructions executed by the simulated cores in aggregate. The cores run a mixture of SPEC marks. Multiple FPGAs actually improve the performance of HAsim beyond a single FPGA, if the number of simulated cores is large enough, and the performance is not worse than 40% of a single FPGA.

## Slide 14: Scratchpads: The LEAP memory abstraction
module memIfc(
mem_ifc
);
bram m0(mem_ifc[0]);
bram m1(mem_ifc[1]);
…
endmodule
module memIfc( mem_ifc,
dram_ifc
);
dram d0(dram_ifc);
dram2bram db0(dram_ifc, mem_ifc[0], bram0)
bram b0 (bram0)
dram2bram db1(dram_ifc, mem_ifc[1], bram1)
bram b1(bram1)
…
endmodule
Like communications, memory is fundamental to programs
HAsim has big memory needs
How is memory specified in RTL?
What if we don’t have enough memory on board?
Added in DRAM mechanically
What if DRAM still isn’t enough?
And what if we don’t have DRAM?

## Slide 15: Scratchpads: A generic memory abstraction
  How should a memory interface look?
  Consider malloc
  Goal: preserve simple interface
  How should we implement?
  Compiler manages resources and plumbing
  Caches, DRAM, and virtual memory all transparent
interface Scratchpad#(addr_t,
data_t);
readReq(addr_t addr);
data_t readResp();
write(addr_t addr,
data_t data);
endinterface
Unlimited Address Space
Arbitrary Data Size
Latency Insensitive

## Slide 16: Scratchpads: Single FPGA
Unlimited Address Space
A
Client
Host Memory
Interface
Off-board I/O
Client
Client
Client
Central
Cache
On-board Memory
Arbitrary number of clients
Fast, Local Cache
Notes: What happens when we scale to multiple FPGAs? In this case, we gain access to more resources, and memory interfaces are tied to the local on-board memories. Since we use LI channels to describe the implementation of the memory service, client memories on a remote FPGA can also be linked to remote cache resources, providing a correct, if slower implementation on those FPGAs which do not have a memory resource.

## Slide 17: Scratchpads: Performance
Chart: Read Bandwidth
| 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576 | 2097152 | 4194304 | 8388608
1 | 0.99998 | 0.99998 | 0.44443 | 0.44443 | 0.484 | 0.43854 | 0.46456 | 0.46975 | 0.46518 | 0.47115 | 0.47111 | 0.46972 | 0.47115 | 0.47115 | 0.47115 | 0.47111
2 | 0.99085 | 0.99657 | 0.49926 | 0.30436 | 0.30485 | 0.30431 | 0.30487 | 0.30373 | 0.096374 | 0.050264 | 0.029847 | 0.029588 | 0.029947 | 0.02976 | 0.029783 | 0.029854
3 | 0.68283 | 0.52206 | 0.28643 | 0.20639 | 0.20501 | 0.20504 | 0.20509 | 0.20506 | 0.10207 | 0.035499 | 0.027575 | 0.028712 | 0.028862 | 0.028753 | 0.028603 | 0.028689
4 | 0.99626 | 0.99297 | 0.15409 | 0.15384 | 0.15384 | 0.15384 | 0.15383 | 0.15382 | 0.066313 | 0.030671 | 0.029015 | 0.031998 | 0.029616 | 0.029638 | 0.030612 | 0.030761
5 | 0.67962 | 0.50733 | 0.21537 | 0.15628 | 0.15383 | 0.15383 | 0.15381 | 0.082938 | 0.05642 | 0.030523 | 0.034598 | 0.034355 | 0.035296 | 0.035162 | 0.034228 | 0.035024
6 | 0.68345 | 0.52358 | 0.21722 | 0.1556 | 0.15382 | 0.15383 | 0.15383 | 0.074863 | 0.04501 | 0.028313 | 0.030803 | 0.03179 | 0.030524 | 0.031709 | 0.031056 | 0.031416
7 | 0.75147 | 0.55071 | 0.21286 | 0.15603 | 0.15383 | 0.15382 | 0.15379 | 0.072347 | 0.046972 | 0.027528 | 0.031196 | 0.031131 | 0.03206 | 0.032654 | 0.031577 | 0.031353
8 | 0.99683 | 0.99103 | 0.15396 | 0.15383 | 0.15384 | 0.15382 | 0.15379 | 0.087866 | 0.0541 | 0.015513 | 0.016036 | 0.016885 | 0.016834 | 0.016269 | 0.017016 | 0.016383
16 | 0.99449 | 0.49829 | 0.1538 | 0.15357 | 0.15351 | 0.15361 | 0.076374 | 0.060824 | 0.030175 | 0.013215 | 0.01333 | 0.013397 | 0.013174 | 0.013346 | 0.013432 | 0.013183
32 | 0.99454 | 0.98823 | 0.15394 | 0.15362 | 0.15365 | 0.094199 | 0.089758 | 0.060132 | 0.026401 | 0.012188 | 0.013359 | 0.013248 | 0.013303 | 0.013685 | 0.013391 | 0.013197
64 | 0.99452 | 0.98928 | 0.15409 | 0.15381 | 0.15374 | 0.11781 | 0.097112 | 0.052834 | 0.038493 | 0.015585 | 0.016562 | 0.016478 | 0.016724 | 0.017312 | 0.016841 | 0.016612
128
Local Cache
Central Cache
Host Memory

## Slide 18: Scratchpads: More FPGAs, more resources
C
B
Inter-FPGA Router
Client
Client
Client
Client
Central Cache
On-board Memory
A
Client
Central Cache
On-board Memory
Inter-FPGA Router
Automatic routing to nearest cache
Scalable support for multiple chip level resources
Remote Access to Resources

## Slide 19: LEAP: Libraries that simplify the use of FPGAs
Memory and communication are fundamental to programs
Libraries simplify programming
LEAP libraries provide several basic functionalities
RTL: FIFOs, memories, caches
System services: configuration, STDIO, statistics, debugging
Portability thru abstraction
All libraries and services use abstraction layers
Each FPGA platform provides some implementation of these layers
FPGA Physical Devices
Virtual Channel Multiplexing
FPGA
Params
STDIO
Starter
Asserts
Scratchpad
Panel
Debug
Stats
Central
Cache
LEAP
Libraries
Marshalling

## Slide 20: Building on abstractions: STDIO Service
Virtual Channel Multiplexing
Kernel Driver
FPGA Physical Devices
Virtual Channel Multiplexing
FPGA
CPU
Marshalling
Marshalling
STDIO Service
STDIO Service
STDIO
Node
User
Module
STDIO
Node
User
Module
STDIO
Node
User
Module
printf()
LINC network
stdio.printf(msg,List::nil);

## Slide 21: Portability: Leveraging abstraction
Virtual Channel Multplexing
ACP Physical Devices
Virtual Channel Multiplexing
FPGA
CPU
Marshaling
Marshaling
STDIO Service
STDIO Service
STDIO
Node
User
Module
STDIO
Node
User
Module
STDIO
Node
User
Module
printf()
stdio.printf(msg,List::nil);
Simulator
void channelToHost(long long data);
XUPV5 Physical Devices
Simulation Physical Devices
ACP Kernel Driver
XUPV5 Kernel Driver
Simulation Driver

## Slide 22: Conclusion
LEAP enables FPGA programmers to focus on programming
Simple primitives for communication and memory eliminate many FPGA-related headaches
Platform abstraction permits portability among FPGA platforms
Automatic partitioning of designs across FPGAs
LEAP provides powerful system libraries, enhancing productivity
Debugging FPGAs by printf 

## Slide 23: Questions?

## Slide 24: AWB: Managing hardware and building systems

## Slide 25: Describing complex systems
  LEAP simplifies the programmer interface to the FPGA
  Changing FPGA targets is as simple as plug-n-play
  But managing code for the FPGA is complicated
  Each FPGA requires a platform-specific set of files
  `ifdef quickly falls over
  LEAP relies on the AWB code management infrastructure to provide these functionalities
FPGA Physical Devices
Virtual Channel Multiplexing
FPGA
Marshaling
STDIO Service
STDIO
Node
User
Module
STDIO
Node
User
Module
STDIO
Node
User
Module

## Slide 26: What is AWB?
  An set of abstractions that enables the plug and play of modules to facilitate design
  A suite of tools to support rapid modular construction and analysis of designs
    GUI and command line interfaces
    Released under GPL (specific projects/models may not be)

## Slide 27: Why Modularity?
Speed of development
Well thought out interfaces => better design
Cooperative development
Sharing components between projects
Improved robustness through reuse
Facilitates design trade-offs, e.g., speed/complexity
Design space experimentation w/o code bloat
Factorial development and evaluation
Notes: Encourages isomorphism to design by enforcing hierarchical representation of the model.

## Slide 28: AWB Projects
AWB
Asim
Alpha
LEAP
HASIM
Airblue
H.264
EV8
EV9
X86
Secret
…
802.11
Softrate
Alpha
Secret
…
…
…

## Slide 29: AWB Glossary
Packages (codebases) - .pack files:
  are stored in repositories and checked out, or
  are referenced locally on a system
  become part of a users local workspaces
  are versioned
  can be grouped into sets called bundles
    which can be checked out together
  contain modules, models (projects) and benchmarks

## Slide 30: AWB Glossary
  Models (projects) - .apm files:
    are a description of a hierarchy of modules
    are turned into a build directory tree via a configuration step
  Benchmarks - .cfg files:
    are a description of a run of a design
    are turned into a run directory tree via a setup step

## Slide 31: AWB Glossary
  Workspaces
    are a place to work on awb-based projects
    can contain multiple packages
    can contain multiple build directories,
      which can contain multiple benchmark runs
http://asim.csail.mit.edu/redmine/projects/awb/wiki/Glossary

## Slide 32: What is the ROI for so much mechanism?
  The layer of abstraction brings distributed modules and tools under one umbrella
  Distinct packages may be independently developed, maintained and access controlled
  Bundles simplify creation of projects that are composed of code from different packages and allow base lining those projects with a specific code revision
  A unified model (project) representation facilitates creation of alternative designs (and build procedures)
  A standardized module representation facilitates code swapability, reuse and creation of reusable build procedures.
  Workspaces organize the simultaneous use of multiple packages and multiple projects over multiple benchmarks.

## Slide 33: AWB Operation Example
Repositories
Workspace

## Slide 34: AWB module details
  Modules represent the unit of “swapability” in source code
  Each module is defined in an .awb file
    Textual %name and %description of the module
    List of the %source files that comprise the module’s code
      E.g., C, C++, BSV, Makefiles or Scons files.
    Modules also %provide an AWB type (different from C++ type)
      E.g., branch_predictor, fetch, decode, execute, cache
    Modules can %require modules of specific AWB types
      E.g., cache may require a pre_fetcher and different prefetch schemes would provide the same AWB type “pre_fetcher”
    Modules can describe %parameters the user can vary
      Parameters can be static (compile time) or dynamic (run time)
Notes: Source code may be a build procedure….

## Slide 35: Module Configuration – Example .awb File
%name APE Unit Tester
%desc APE – The AWB Plugin Exerciser
%attributes ape test
%provides system
%requires feeder ape_driver isa
%source –-public ape.h
%source –-private ape.cpp ape-util.cpp
%param MAX_INST_BUF_SZ 1024 “Number of instr buffer entries”
%param --global MAX_IDLE_CYCLES 256 “Maximum number of idle cycles”
http://asim.csail.mit.edu/redmine/projects/awb/wiki/Awb_file

## Slide 36: Modules
  Multiple modules may have the same awb type, but must have unique %names.
  If two modules provide the same awb type then this is an assertion that they can be swapped for one another and that the result will be a coherent set of code that will successfully build.

## Slide 37: From Modules to Models
  A model (project) is an interesting configuration selected by the user:
    All parameter values are set (unset ones use their default)
    All “requires” choices are made between alternative modules
    Stored in a .apm file
  Created using apm-edit GUI

## Slide 38: Example Module Hierarchy
S
M
C
N
D
R
X
C
W
F
B
Notes: Fundamental components – module
Hierarchical
Specifies a type of module

## Slide 39: Simple Example: Module Selection
B
B
B
B
S
M
C
N
D
R
X
C
W
F
B
B
Notes: Can select a specific implementation of a module

## Slide 40: Complete Example: Module Selection
D
R
X
C
W
F
D
R
X
C
W
F
S
M
C
N
C
M
N
S
B
B
B
B
B
B

## Slide 41: Default Choices via Attributes
B
B
B
B
S
M
C
N
D
R
X
C
W
F
B
X

## Slide 42: Workspace Structure
<workspace-name>/
awb.config - configuration file for this workspace
src/ - area for checked out packages
<package-A>/
  <package-B>/...
build/ - area where models are built and run <project-A>/...
pm/ - source build tree
    obj/ - object tree of built objects
    src/ - source tree (links to module sources)
    <model> - built executable of model
    Makefile - synthesized Makefile
    bm/ - area where benchmarks are run
    <benchmark-A>/...
    run/ - area where experiments/regressions run
http://asim.csail.mit.edu/redmine/projects/awb/wiki/Glossary#Workspace
Notes: “build” area is managed asim tools. The areas inside a package are more user controlled.

## Slide 43: Awb.config file format
[Global]
VERSION=1.4
Class=Asim::Workspace
[Vars]
shared=/usr/share/asim/packages
[Paths]
# Directory containing actual benchmarks
BENCHMARKDIR=/usr/share/asim/benchmarks
# Path where we search for ASIM files
SEARCHPATH=src/leap:…:${shared}/awb/HEAD
[Build]
# Make flags for all model builds
MAKEFLAGS=
Options for many tools that can be inserted in awb.config can be obtained via –options switch, e.g.,
% awb-run –options
[awb-run]
BUILD=1
BUILD_ALL=0
BUILD_DISTCC=0
…
Search for options proceeds from:
<workspace>/awb.config
~/.asim/asimrc
<prefix>/etc/asim/asimrc
http://asim.csail.mit.edu/redmine/projects/awb/wiki/Awbconfig

## Slide 44: Repositories
The CVS, SVN, or GIT repositories described in: 1) ~/.asim/repositories.d/<package-name>.pack 2) <prefix>/etc/asim/repositories.d/<package-name>.pack 3) <prefix>/etc/asim/asim.pack
Check out with command:
  % awb-shell checkout package <pkg-name>[/<version>]
Get updates with command:
  % awb-shell update package <pkg-name>|all
Commit changes with command:
  % awb-shell commit package <pkg-name>|all
http://asim.csail.mit.edu/redmine/projects/awb/wiki/AWB_example_setup_command_line
Notes: Prerequisites
– cvs “login” to repository for anonymous access
- ssh key setup…

## Slide 45: Package Structure Details
<package-name>/
  admin/ - awb-managed administrative files
  config/
  pm/ - model configurations …/…/<model-A>.apm …/…/<model-B>.apm
  bm/ - benchmark configurations …/…/<benchmark-A>.cfg …/…/<benchmark-B>.cfg
modules/ - modules
…/…/<module-A>/ <module-A>.awb - module description <module-A>.h - module source <module-A>.cpp
<module-A>.bsv
<miscelaneous>/ - package specific directories
http://asim.csail.mit.edu/redmine/projects/awb/wiki/Glossary#Package

## Slide 46: Manipulating the Search Path
Automatic:
  Checking out/using a package adds it to the path by default
Semi-automatic
  Run command:
    % awb-shell add package <directory>
Manual
  Edit awb.config

## Slide 47: Model Build
Since a model is created from a pool of modules, the build paradigm adds a new step to “configure” a model source tree from that pool of modules.
Therefore a workspace has:
  A “source” area with a pool of module sources where users add modules and make changes to existing modules…
  A “build” area for “configured” models that is managed almost entirely by the awb infrastructure…filled with build trees populated with links to the actual source files and synthesized source files.
  Note: the actual tool used to do the configure is determined by the ‘type’ of the model.
Notes: Within the directory of a particular model in the build area you see essentially a normal source tree.
Source area also has configuration files for configuring models and describing benchmarks.

## Slide 48: Model Configurations
Found in: config/pm/.../<model>.apm
Contains:
  module hierarchy
  module parameters
To perform the configure a project, cd into your workspace and type:
% awb

## Slide 49: AWB- GUI
The ‘configure’ button invokes the proper configure tool as determined by the model type. (See apm-edit for details)

## Slide 50: AWB- GUI
Runlog shows the command line tool invoked. Should have been leap-configure, which creates a build directory.

## Slide 51: AWB- GUI
The ‘build’ button invokes ‘make’ (or ‘scons’) in the build tree created by the configure script.

## Slide 52: AWB- GUI
The ‘setup’ button invokes the proper benchmark setup tool as determined by the model type. (See apm-edit for details)

## Slide 53: AWB- GUI
The ‘run’ button invokes the ./run script in the benchmark directory created by the benchmark setup script.

## Slide 54: AWB- GUI
http://asim.csail.mit.edu/redmine/projects/awb/wiki/AWB_example_build_GUI

## Slide 55: Awb-shell
% awb-shell
awb> configure model <model>
awb> build model
awb> setup benchmark <benchmark>
awb> run benchmark
awb> quit
Example:
<model> = config/pm/leap/demos/hello/hello_hybrid_exe.apm <benchmark> = config/bm/leap/demos.cfx/benchmarks/null.cfg
http://asim.csail.mit.edu/redmine/projects/awb/wiki/AWB_example_build_command_line

## Slide 56: Apm-edit - GUI

## Slide 57: Apm-edit - GUI
Alternative module operation – replace module in tree with module or submodel
Module properties operations - edit module, open shell in module’s source directory.
Notes: Operations – replace module in tree, edit module, open shell in module’s source directory.

## Slide 58: Spare Slides

## Slide 59: Hello World on a FPGA
FPGA Board
FPGA Chip
Host Processor
CPU/Memory
FPGA code written in Bluespec
FPGA
Application
Block RAM
On-board RAM
Software
Application
Channel
Channel
Outputs
Inputs
Memory
Physical
Logical
Notes: Platform Assumptions
  Hybrid host system with an FPGA and a CPU
  Hybrid application with an FPGA and a software component
    Application invoked from software
    Parameters sent from software to FPGA
    FPGA output sent to software that displays it on stdout

## Slide 60: Solving the FPGA via Abstraction
Implement a Channel
  Identify and multiplex multiple client modules
  LEAP Abstraction: Channel IO
Make the Channel more useful
  Chunk and marshal typed messages
  Syntactic sugar
  LEAP Abstraction: Remote Request Response (RRR)
Build high-level Services
  LEAP Abstraction: Soft Services

## Slide 61: Solving Problems via Abstraction
Implement a Channel
  Identify and multiplex multiple client modules
  LEAP Abstraction: Channel IO
Make the Channel more useful
  Chunk and marshal typed messages
  Syntactic sugar
  LEAP Abstraction: Remote Request Response (RRR)
Build high-level Services
  LEAP Abstraction: Soft Services

## Slide 62: LEAP Abstraction Layers: Channel IO
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
Channel 0
Channel 1
Channel 1
Channel 0
FPGA
CPU

## Slide 63: Solving Problems via Abstraction
Implement a Channel
  Identify and multiplex multiple client modules
  LEAP Abstraction: Channel IO
Make the Channel more useful
  Chunk and marshal typed messages
  Syntactic sugar
  LEAP Abstraction: Remote Request Response (RRR)
Build high-level Services
  LEAP Abstraction: Soft Services
[ Parashar et. al., WARP 2008 ]

## Slide 64: RRR Specification Language
// ----------------------------------------
// create a new service called ISA_EMULATOR
// ----------------------------------------
service ISA_EMULATOR
{
// --------------------------------
// declare services provided by CPU
// --------------------------------
server CPU <- FPGA;
{
method UpdateRegister(in REG_INDEX, in REG_VALUE);
method Emulate(in INST_INFO, out INST_ADDR);
};
// ---------------------------------
// declare services provided by FPGA
// ---------------------------------
server FPGA <- CPU;
{
method SyncRegister(in REG_INDEX, in REG_VALUE);
};
};

## Slide 65: LEAP Abstraction Layers: RRR
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
FPGA
CPU

## Slide 66: LEAP Abstraction Layers: RRR
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
FPGA
CPU
Client Stub
Server Stub
RRR
specification
files

## Slide 67: LEAP Abstraction Layers: RRR
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
FPGA
CPU
ClientStubs.ISA_EMULATOR iemu;
...
...
iemu.UpdateRegister.Request(
REG_R27, regFile[REG_R27]);
...
...
iemu.Emulate.Request(inst);
...
...
tgtPC <- iemu.Emulate.Response();
ISA_EMULATOR::UpdateRegister(
REG_INDEX i,
REG_VALUE v)
{
regFile[i] = v;
}
ISA_EMULATOR::Emulate(
INST_INFO inst)
{
// emulate the instruction
return target_PC;
}
Client Stub
Server Stub
User Code
User Code

## Slide 68: LEAP Abstraction Layers: RRR
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
FPGA
CPU
Stub
Stub
Stub
Stub
Stub
Stub
User Application

## Slide 69: Modularity in FPGA Accelerators
Viterbi
SOVA
BCJR
Airblue 802.11g
Debug Out
PCIe
PHY
RX Pipeline
TX Pipeline
Error Correction
A bug!
  Add debugging logic
  Route to Debug Out

## Slide 70: The Modularity Problem
Error Correction
Airblue 80211.g
PHY
RX Pipeline
Branch
Pred
BCJR
How many modules change?
Alternatives can worsen problem
  What if alternatives give different insight?
  Worst case: work grows multiplicatively
Debug Out
PCIe
TX Pipeline
A bug!
  Add debugging logic
  Route to Debug Out
Notes: Verilog OOMRs not satisfactory
  Break the modular abstraction
  Requires “Debug Out” to have knowledge of CPU, Front End, etc
  SystemVerilog IFCs only partial solution

## Slide 71: LEAP Abstraction: Soft Connections
Create channel between BCJR and Debug
  Identify endpoints with text string
  Have HDL compiler make the connection
  Connection acts like a queue (guarded output FIFO)
Airblue 802.11g
Debug Out
PCIe
PHY
RX Pipeline
TX Pipeline
Error Correction
BCJR
send( )
“debug_info”
recv( )
“debug_info”
Added during compilation
[ Pellauer et. al., DAC 2009 ]
debugConn = mkSend(“debug_info”);
.
if (bad_thing_happened && debugConn.notFull)
debugConn.send(interesting_info);
connFromPHY = mkRecv(“debug_info”);
.
if (connFromPHY.notEmpty) {
pcie.xfer(connFromPHY.first);
connFromPHY.deq();
}

## Slide 72: Solving Problems via Abstraction
Implement a Channel
  Identify and multiplex multiple client modules
  LEAP Abstraction: Channel IO
Make the Channel more useful
  Chunk and marshal typed messages
  Syntactic sugar
  LEAP Abstraction: Remote Request Response (RRR)
Build high-level Services
  LEAP Abstraction: Virtual Services and Devices

## Slide 73: LEAP Abstraction Layers: Services
Channel IO
Kernel Driver
FPGA Platform Physical Devices
Channel IO
FPGA
CPU
Stub
Stub
Stub
Stub
Stub
Stub
Params
STDIO
Starter
Asserts
Scratchpad
Panel
Debug
Stats
Central
Cache
Params
STDIO
Starter
Asserts
Scratchpad
Panel
Debug
Stats
Platform
Services